## Slide 1
硬體安全導論
Final Project
第二組
106000147 沈永聖 106061247 林均容 106061252劉育瑋 106061255 陳孟泰
01
資料蒐集
Sample size
蒐集方法
02
參數設定
參數設定
03
結果與分析
Pass rate
分析
04
Quality of TRNG
Quality of TRNG

## Slide 2
大綱
01
資料蒐集
Sample size
蒐集方法
02
參數設定
參數設定
03
結果與分析
Pass rate
分析
04
Quality of TRNG
Quality of TRNG

## Slide 3
01
資料蒐集
Sample size
蒐集方法
02
參數設定
參數設定
03
結果與分析
Pass rate
分析
04
Quality of TRNG
Quality of TRNG

## Slide 4
如何選擇X與Y?
資料蒐集
Sample size
蒐集方法
02
參數設定
參數設定
03
結果與分析
Pass rate
分析
04
Quality of TRNG
Quality of TRNG
01

## Slide 5
Sample size -如何選擇X?
Test | Length of sequence(n) | block size | length of template
Frequency Test | >100 | None | None
Frequency Test within a Block | >100 | M>=20, M > 0.01n | None
Runs Test | >100 | None | None
Longest-Run-of-Ones in a Block | 看圖 | None | None
Rank Test | >=38912(QM) | None | None
DFT Test | >1000 | None | None
Non-overlapping Template Matching Test | None | M > 0.01n | m = 9, 10
Overlapping Template Matching Test | >10^6 | None | m = 9, 10
Universal Statistical" Test | 看圖 | None | None
Linear Complexity Test | >10^6 | 500~5000 | None
Serial Test | None | m < log_2(n) - 2 | None
Approximate Entropy Test | None | m < log_2(n) - 5 | None
Cumulative Sums (Cusums) Test | >100 | None | None
Random Excursions Test | >10^6 | None | None
Random Excursions Variant Test | >10^6 | None | None
Longest Run-of-Ones in a Block
Universal Statistical Test
01

## Slide 6
Sample size -如何選擇X?
Test | Length of sequence(n) | block size | length of template
Frequency Test | >100 | None | None
Frequency Test within a Block | >100 | M>=20, M > 0.01n | None
Runs Test | >100 | None | None
Longest-Run-of-Ones in a Block | 看圖 | None | None
Rank Test | >=38912(QM) | None | None
DFT Test | >1000 | None | None
Non-overlapping Template Matching Test | None | M > 0.01n | m = 9, 10
Overlapping Template Matching Test | >10^6 | None | m = 9, 10
Universal Statistical" Test | 看圖 | None | None
Linear Complexity Test | >10^6 | 500~5000 | None
Serial Test | None | m < log_2(n) - 2 | None
Approximate Entropy Test | None | m < log_2(n) - 5 | None
Cumulative Sums (Cusums) Test | >100 | None | None
Random Excursions Test | >10^6 | None | None
Random Excursions Variant Test | >10^6 | None | None
Longest Run-of-Ones in a Block
Universal Statistical Test
01

## Slide 7
Sample size -如何選擇X?
Longest Run-of-Ones in a Block
Universal Statistical Test
01

## Slide 8
Sample size -如何選擇Y?
01
Baud rate = 115200 bits/s
100 files

## Slide 9
如何選擇X與Y?
Baud rate = 115200 bits/s
100 files
資料蒐集
Sample size
蒐集方法
參數設定
參數設定
結果與分析
Pass rate
分析
Quality of TRNG
Quality of TRNG
01

## Slide 10
01
資料蒐集
Sample size
蒐集方法
02
參數設定
參數設定
03
結果與分析
Pass rate
分析
04
Quality of TRNG
Quality of TRNG

## Slide 11
參數設定
01
資料蒐集
Sample size
蒐集方法
02
參數設定
參數設定
03
結果與分析
Pass rate
分析
04
Quality of TRNG
Quality of TRNG

## Slide 12
Test | Length of sequence(n) | block size | length of template
Frequency Test | >100 | None | None
Frequency Test within a Block | >100 | M>=20, M > 0.01n | None
Runs Test | >100 | None | None
Longest-Run-of-Ones in a Block | 看圖 | None | None
Rank Test | >=38912(QM) | None | None
DFT Test | >1000 | None | None
Non-overlapping Template Matching Test | None | M > 0.01n | m = 9, 10
Overlapping Template Matching Test | >10^6 | None | m = 9, 10
Universal Statistical" Test | 看圖 | None | None
Linear Complexity Test | >10^6 | 500~5000 | None
Serial Test | None | m < log_2(n) - 2 | None
Approximate Entropy Test | None | m < log_2(n) - 5 | None
Cumulative Sums (Cusums) Test | >100 | None | None
Random Excursions Test | >10^6 | None | None
Random Excursions Variant Test | >10^6 | None | None
參數設定
02

## Slide 13
參數設定
02

## Slide 14
01
資料蒐集
Sample size
蒐集方法
02
參數設定
參數設定
03
結果與分析
Pass rate
分析
04
Quality of TRNG
Quality of TRNG

## Slide 15
03
Pass? Fail? For a Specific subtest
188 subtests for each binary sequence (file)
Proportion of (sub)Sequences Passing a Test
Confidence Interval:
Uniform Distribution of P-values
01
資料蒐集
Sample size
蒐集方法
02
參數設定
參數設定
結果與分析
Pass rate
分析
04
Quality of TRNG
Quality of TRNG

## Slide 16
03
Pass Rate
Rate of sufficiently random sequence generated from an RNG
Sufficiently random: Pass all subtests in NIST SP900-22
Pass Rate for the collected random number sequences: 50%

## Slide 17
03
Possible Reasons for Failure

## Slide 18
03
Insufficient Length of Sequence
Test | Length of sequence(n) | # of Fails | # of Subtests
Frequency Test | >100 | 0 | 1
Frequency Test within a Block | >100 | 0 | 1
Runs Test | >100 | 0 | 1
Longest-Run-of-Ones in a Block | 904,960 ~ 2,068,480 (in our case) | 2 | 1
Rank Test | >=38912(QM) | 0 | 1
DFT Test | >1000 | 0 | 1
Non-overlapping Template Matching Test | None | 39 | 148
Overlapping Template Matching Test | >10^6 | 0 | 1
Universal Statistical" Test | >=750,000 (in our case) | 1 | 1
Linear Complexity Test | >10^6 | 1 | 1
Serial Test | None | 2 | 2
Approximate Entropy Test | None | 1 | 1
Cumulative Sums (Cusums) Test | >100 | 0 | 1
Random Excursions Test | >10^6 | 6 | 8
Random Excursions Variant Test | >10^6 | 2 | 18

## Slide 19
03
Parameter-Dependant Tests
Test | Length of sequence(n) | Block size | Length of template | # of Fails | # of Subtests
Frequency Test | >100 | None | None | 0 | 1
Frequency Test within a Block | >100 | M > 0.01n | None | 0 | 1
Runs Test | >100 | None | None | 0 | 1
Longest-Run-of-Ones in a Block | 看圖 | None | None | 2 | 1
Rank Test | >=38912(QM) | None | None | 0 | 1
DFT Test | >1000 | None | None | 0 | 1
Non-overlapping Template Matching Test | None | M > 0.01n | m = 9, 10 | 39 | 148
Overlapping Template Matching Test | >10^6 | None | m = 9, 10 | 0 | 1
Universal Statistical" Test | 看圖 | None | None | 1 | 1
Linear Complexity Test | >10^6 | 500~5000 | None | 1 | 1
Serial Test | None | m < log_2(n) - 2 | None | 2 | 2
Approximate Entropy Test | None | m < log_2(n) - 5 | None | 1 | 1
Cumulative Sums (Cusums) Test | >100 | None | None | 0 | 1
Random Excursions Test | >10^6 | None | None | 6 | 8
Random Excursions Variant Test | >10^6 | None | None | 2 | 18

## Slide 20
03
Parameter-Dependant Tests
Non-overlapping Template Matching Test:
m=9 -> 148 kinds of 9-bit patterns -> 148 subtests
Serial Test:
We select m=16; Recommended m < – 2=18
Approximate Entropy Test:
We select m=12; Recommended m < – 5=15

## Slide 21
03
Selection of Sample Size (Y)
100 files * 100 * 2^20 bits
50 files * 200 * 2^20 bits

## Slide 22
03
Selection of Sample Size (Y)
Sample size should be on the order of the inverse of the significance level (α) -> α = 0.01 -> Y >=100
The larger Y we use, the larger the tolerance of the # of low-quality RN subsequences
Calculate accepted lower bound of the confidence interval:
Y=100: 100*(0.99-0.0298)=96.0=96(in NIST test)
Y=200: 200*(0.99-0.0211)=193.8=193(in NIST test)
*Y=1000: 1000*0.9805=980

## Slide 23
03
Tests Often Fail

## Slide 24
03
Non-overlapping Template Matching Test
39 fails in 100 files (39%)
54 fails in (148 subtests (m=9) * 100 files) (0.36%)
A common reason for a sequence to be rejected as a random one, but not common for failing a subtest.

## Slide 25
03
Purpose and Test Description
Detect generators that produce too many occurrences of a given non-periodic pattern.
An m-bit window is used to search for a specific m-bit pattern. If matches, counter +1.
A measure of how well the observed number of template “hits” matches the expected number of template “hits” (under an assumption of randomness) -> consequent P-value

## Slide 26
03
Why Fail and How to Improve
Reason
A small sample size (Y=100)
Too many (148) subtests under recommended m=9 (9-bit pattern)
Solution (in statistical way)
Larger Y
m=8, 7, 6…
Ask NIST to replace the results of these 148 subtests with fewer outcomes, or say, do some further statistical calculation among the 148 results instead of directly 148 P-values for a subsequence.

## Slide 27
03
Why Argue an Advanced Non-overlapping Template Matching Test is needed ?
High correlation between the tests with some tested patterns
The correlation coefficients can be computed as ρ(001010101, 010101011) = 0.652525 and ρ(001010101, 101010100) = 0.3212—from Atsushi Iwasaki, “Independent Randomness Tests based on the Orthogonalized Non-overlapping Template Matching Test”, 2019

## Slide 28
03
Tests for the
Longest-Run-of-Ones in a Block

## Slide 29
03
Example
Number of sequences |  | 100 | 200
Total Fails |  | 50% | 20%
Test | Subtest # | Fail # | 
Frequency Test | 1 | 0 | 0
Frequency Test within a Block | 1 | 0 | 0
Runs Test | 1 | 0 | 0
Longest-Run-of-Ones in a Block | 1 | 2 | 0
Rank Test | 1 | 0 | 0
DFT Test | 1 | 0 | 0
Non-overlapping Template Matching Test | 148 | 39 | 5
Overlapping Template Matching Test | 1 | 0 | 0
Universal Statistical Test | 1 | 1 | 1
Linear Complexity Test | 1 | 1 | 0
Serial Test | 2 | 2 | 1
Approximate Entropy Test | 1 | 1 | 0
Cumulative Sums (Cusums) Test | 2 | 0 | 0
Random Excursions Test | 8 | 6 | 5
Random Excursions Variant Test | 18 | 2 | 0

## Slide 30
03
Example
n : The length of the bit string. (128)
M : The length of each block. (8)
N : The number of blocks. (16)
input = 11001100000101010110110001001100111000000000001001001101010100010001001111010110100000001101011111001100111001101101100010110010
Subblock | Max-run | Subblock | Max-run
11001100 | 2 | 00010101 | 1
01101100 | 2 | 01001100 | 2
11100000 | 0 | 00000010 | 1
01001101 | 2 | 01010001 | 1
00010011 | 2 | 11010110 | 2
10000000 | 1 | 11010111 | 3
11001100 | 2 | 11100110 | 3
11011000 | 2 | 10110010 | 2
= 4 | = 9 | = 3 | = 0
= 4.882457 |  | P = 0.180609 | 
P-value ≥ 0.01, accept the sequence as random |  |  | 
Subblock | Max-run | Subblock | Max-run
11001100 | 2 | 00010101 | 1
01101100 | 2 | 01001100 | 2
11100000 | 0 | 00000010 | 1
01001101 | 2 | 01010001 | 1
00010011 | 2 | 11010110 | 2
10000000 | 1 | 11010111 | 3
11001100 | 2 | 11100110 | 3
11011000 | 2 | 10110010 | 2
 |  | P = 0.180609 | 
P-value ≥ 0.01, accept the sequence as random |  |  | 

## Slide 31
03
Random Excursions Test

## Slide 32
03
Test Purpose
The number of cycles having exactly K visits in a cumulative sum random walk
Cumulative sum random walk
A cycle of a random walk
To determine if the number of visits to a particular state within a cycle deviates from what one would expect for a random sequence. This test is actually a series of eight tests (and conclusions), one test and conclusion for each of the states: -4, -3, -2, -1 and +1, +2, +3, +4.

## Slide 33
03
Test Description
Form a normalized (-1, +1) sequence X: The zeros and ones of the input sequence (ε) are changed to values of –1 and +1 via Xi = 2εi – 1.
Compute the partial sums Si of successively larger subsequences, each starting with X1. Form the set S ={Si}.
Form a new sequence S' by attaching zeros before and after the set S. That is, S' = 0, s1, s2, … , sn,0.
Let J = the total number of zero crossings in S‘, where a zero crossing is a value of zero in S ’ that occurs after the starting zero. J is also the number of cycles in S′

## Slide 34
03
Test Description
For each cycle and for each non-zero state value x having values –4 ≤x ≤-1 and 1 ≤x ≤4, compute the frequency of each x within each cycle.
For each of the eight states of x, compute νk(x) = the total number of cycles in which state x occurs exactly k times among all cycles, for k = 0, 1, …, 5 (for k = 5, all frequencies ≥ 5 are stored in ν5(x)).
For each of the eight states of x, compute the test statistic.
For each state of x, compute P-value = igamc(5/2, (obs)/2). Eight P-values will be produced.

## Slide 35
03
Example

## Slide 36
03
Example
when x=1 :
(obs) = 4.333033
P-value =
0.502529 ≧ 0.01
→ the sequence is random

## Slide 37
03
Why Fail and How to Improve
If the computed P-value is < 0.01, then conclude that the sequence is non-random. Otherwise, conclude that the sequence is random.
Reason :
P-value formulas may result in bogus values due to difficulties arising from numerical approximations.
Improve the P-value formulas may improve the results.

## Slide 38
01
資料蒐集
Sample size
蒐集方法
02
參數設定
參數設定
03
結果與分析
Pass rate
分析
04
Quality of TRNG
Quality of TRNG

## Slide 39
04
Quality of TRNG

## Slide 40
Thank You for Listening
04

## Slide 41
Q&A